Table S4: Estimated standard uncertainty (1 ) of dose to water at the phantom surface.

| Type of quantity or procedure | % Uncertainty, TG-61 | % Uncertainty, this work |
| --- | --- | --- |
| Air-kerma calibration factor, (cGy/nC) | 0.7 | 2.3 |
| Effect of beam quality difference between calibration measurement | 2.0 | 2.0 |
| Backscatter factor, | 1.5 | 10.0 |
| Chamber stem correction factor, | 1.0 | 1.0 |
| Mass energy-absorption coefficients, | 1.5 | 1.5 |
| In-air measurement in the user’s beam | 1.5 | 1.5 |
| Combined standard uncertainty | 3.5 | 10.7 |