|  | CO2 | ethanol |
| --- | --- | --- |
| Channel | A | B |
| Column | PPU | OV-1 |
| Method acquisition parameters |
| Column temperature (°C) | 140 | 100 |
| Sampling time (s) | 10 |
| Injection time (ms) | 50 |
| Detector sensibility | low | high |
| Running time (s) | 60 |
| Peak integration parameters |
| Slope sensitivity (µV/s) | 5.00 |
| Peak width (s) | 0.50 |
| Integration OFF at time (s) | 0.00 | 0.00 |
| Integration ON at time (s) | 23.50 | 30.00 |

Table S1: Listing of the chromatographic parameters used for the simultaneous analysis of CO2 and ethanol above the free surface of champagne glasses (redrawn from [39]).