Repeatability of and relationship between potential COPD biomarkers in bronchoalveolar lavage, bronchial biopsies, serum, and induced sputum

Manuscript Online Supplement

### Analysis of Urine samples

Urine (0.5 ml) was mixed with 0.5 ml 0.1 M HCL, centrifuged (5 min, 10g), and applied to a 3 ml MCX cation-exchange column (Oasis, Waters, prewashed with 0.5 ml MeOH, 0.5 ml H2O and 0.5 ml 0.05 M HCL). After washing (2x 1 ml 0.05 M HCL and 4x 1 ml water) and elution (3x 0.1 ml 2M HCL), the eluate was evaporated (40°C under vacuum). The dry residue was dissolved in 1ml 0.1% formic acid and centrifuged. The clear supernatant was used for liquid chromatography-electronspray ionisation-mass spectrometry (LC-ESI-MS) analysis.

### Ionexchange Chromatography:

Column:	ProPac SCX-10 2 x 250 mm (Dionex)

Solvents:	A: 0.1% Formic Acid, B: 1% NH3 in Water

Flow:		0.5 ml/min, temperature:	40°C

Gradient:	t(min)	%A	%B

0	100	0

1	100	0

5	80	20

7	0	100

7.1	0	100

7.5	100	0

20	100	0

Retention time: Desmosin and Isodesmosin (not separated): 6.2 min

### RP Chromatography:

Column:	Atlantis T3 3µm 2.1 x 100 mm (Waters)

Solvents:	A: 5 mM ammonia acetate + 7 mM HFBA, 	B: Methanol / Solvent A 80/20

Flow:		0.5 ml/min, temperature:	50°C

Gradient:	t(min)	%A	%B

0	100	0

1	100	0

9	70	30

10	0	100

11	0	100

11.5	100	0

15	100	0

Retention time: Isodesmosin:	6.2 min

Retention time: Desmosin: 	6.7 min